## Slide 1
Hex | Decimal | Binary | Comment
0A | 16 | 0000 1010 | MAX31856_CJTH_REG
7F | 127 | 0111 1111 | 
FF | 255 | 1111 1111 | 
00 | 0 | 0000 0000 | 
80 | 128 | 1000 0000 | 
MAX31856 SPI Notes
Bit Number |  |  |  |  |  |  | 
MSB |  |  |  |  |  |  | LSB
A7 | A6 | A5 | A4 | A3 | A2 | A1 | A0
A7 = 0 – One or more byte reads will follow the address byte
A7 = 1 – One or more byte writes will follow the address byte
If data continues to be clocked in or out, the address will loop from 7Fh/FFh to 00h/80h.
Invalid memory addresses report an FFh value.
Attempting to write to a read-only register will result in no change to that register’s contents.

## Slide 2
Address | Binary | Read/Write | Name | Factory Default | Binary | Function
00h/80h | 0000 0000 / 1000 0000 | Read/Write | CR0 | 00h | 0000 0000 | Configuration 0 Register
01h/81h | 0000 0001 / 1000 0001 | Read/Write | CR1 | 03h | 0000 0011 | Configuration 1 Register
0Ah/8Ah | 0000 1010 / 1000 1010 | Read/Write | CJTH | 00h | 0000 0000 | Cold-Junction Temperature Register, MSB
0Bh/8Bh | 0000 1011 / 1000 1011 | Read/Write | CJTL | 00h | 0000 0000 | Cold-Junction Temperature Register, LSB
Register Memory Map
#define MAX31856_CR0_REG 0x00 ///< Config 0 register
#define MAX31856_CR0_AUTOCONVERT 0x80 ///< Config 0 Auto convert flag
#define MAX31856_CR0_1SHOT 0x40 ///< Config 0 one shot convert flag
#define MAX31856_CR0_OCFAULT1 0x20 ///< Config 0 open circuit fault 1 flag
#define MAX31856_CR0_OCFAULT0 0x10 ///< Config 0 open circuit fault 0 flag
#define MAX31856_CR0_CJ 0x08 ///< Config 0 cold junction disable flag
#define MAX31856_CR0_FAULT 0x04 ///< Config 0 fault mode flag
#define MAX31856_CR0_FAULTCLR 0x02 ///< Config 0 fault clear flag
#define MAX31856_CR1_REG 0x01 ///< Config 1 register
#define MAX31856_MASK_REG 0x02 ///< Fault Mask register
#define MAX31856_CJHF_REG 0x03 ///< Cold junction High temp fault register
#define MAX31856_CJLF_REG 0x04 ///< Cold junction Low temp fault register
#define MAX31856_LTHFTH_REG 0x05 ///< Linearized Temperature High Fault Threshold Register, MSB
#define MAX31856_LTHFTL_REG 0x06 ///< Linearized Temperature High Fault Threshold Register, LSB
#define MAX31856_LTLFTH_REG 0x07 ///< Linearized Temperature Low Fault Threshold Register, MSB
#define MAX31856_LTLFTL_REG 0x08 ///< Linearized Temperature Low Fault Threshold Register, LSB
#define MAX31856_CJTO_REG 0x09 ///< Cold-Junction Temperature Offset Register
#define MAX31856_CJTH_REG 0x0A ///< Cold-Junction Temperature Register, MSB
#define MAX31856_CJTL_REG 0x0B ///< Cold-Junction Temperature Register, LSB
#define MAX31856_LTCBH_REG 0x0C ///< Linearized TC Temperature, Byte 2
#define MAX31856_LTCBM_REG 0x0D ///< Linearized TC Temperature, Byte 1
#define MAX31856_LTCBL_REG 0x0E ///< Linearized TC Temperature, Byte 0
#define MAX31856_SR_REG 0x0F ///< Fault Status Register
#define MAX31856_FAULT_CJRANGE 0x80 ///< Fault status Cold Junction Out-of-Range flag
#define MAX31856_FAULT_TCRANGE 0x40 ///< Fault status Thermocouple Out-of-Range flag
#define MAX31856_FAULT_CJHIGH 0x20 ///< Fault status Cold-Junction High Fault flag
#define MAX31856_FAULT_CJLOW 0x10 ///< Fault status Cold-Junction Low Fault flag
#define MAX31856_FAULT_TCHIGH 0x08 ///< Fault status Thermocouple Temperature High Fault flag
#define MAX31856_FAULT_TCLOW 0x04 ///< Fault status Thermocouple Temperature Low Fault flag
#define MAX31856_FAULT_OVUV 0x02 ///< Fault status Overvoltage or Undervoltage Input Fault flag
#define MAX31856_FAULT_OPEN 0x01 ///< Fault status Thermocouple Open-Circuit Fault flag
0x40 = 0100 0000

## Slide 3
/**************************************************************************/
/*!
@brief Return cold-junction (internal chip) temperature
@returns Floating point temperature in Celsius
*/
/**************************************************************************/
float Adafruit_MAX31856::readCJTemperature(void) {
return readRegister16(MAX31856_CJTH_REG) / 256.0;
}
uint16_t Adafruit_MAX31856::readRegister16(uint8_t addr) {
uint8_t buffer[2] = {0, 0};
readRegisterN(addr, buffer, 2);
uint16_t ret = buffer[0];
ret <<= 8;
ret |= buffer[1];
return ret;
}
#define MAX31856_CJTH_REG 0x0A ///< Cold-Junction Temperature Register, MSB
Hex | Decimal | Binary | Comment
0A | 16 | 0000 1010 | MAX31856_CJTH_REG
7F | 127 | 0111 1111 | 
void Adafruit_MAX31856::readRegisterN(uint8_t addr, uint8_t buffer[],
uint8_t n) {
addr &= 0x7F; // MSB=0 for read, make sure top bit is not set
spi_dev.write_then_read(&addr, 1, buffer, n);
}
Read Cold Junction Temperature
Bitwise AND
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 1
addr
0x7F
Addr &= 0x7F
Bits 6 -0 are unchanged, only bit 7 is forced to 0
/*!
* @brief Write some data, then read some data from SPI into another buffer.
* The buffers can point to same/overlapping locations. This does not
* transmit-receive at the same time!
* @param write_buffer Pointer to buffer of data to write from
* @param write_len Number of bytes from buffer to write.
* @param read_buffer Pointer to buffer of data to read into.
* @param read_len Number of bytes from buffer to read.
* @param sendvalue The 8-bits of data to write when doing the data read,
* defaults to 0xFF
* @return Always returns true because there's no way to test success of SPI
* writes
*/
bool Adafruit_SPIDevice::write_then_read(uint8_t *write_buffer,
size_t write_len, uint8_t *read_buffer,
size_t read_len, uint8_t sendvalue) {
if (_spi) {
_spi->beginTransaction(*_spiSetting);
}
digitalWrite(_cs, LOW);
// do the writing
for (size_t i = 0; i < write_len; i++) {
transfer(write_buffer[i]);
}
#ifdef DEBUG_SERIAL
DEBUG_SERIAL.print(F("\tSPIDevice Wrote: "));
for (uint16_t i = 0; i < write_len; i++) {
DEBUG_SERIAL.print(F("0x"));
DEBUG_SERIAL.print(write_buffer[i], HEX);
DEBUG_SERIAL.print(F(", "));
if (write_len % 32 == 31) {
DEBUG_SERIAL.println();
}
}
DEBUG_SERIAL.println();
#endif
// do the reading
for (size_t i = 0; i < read_len; i++) {
read_buffer[i] = transfer(sendvalue);
}
#ifdef DEBUG_SERIAL
DEBUG_SERIAL.print(F("\tSPIDevice Read: "));
for (uint16_t i = 0; i < read_len; i++) {
DEBUG_SERIAL.print(F("0x"));
DEBUG_SERIAL.print(read_buffer[i], HEX);
DEBUG_SERIAL.print(F(", "));
if (read_len % 32 == 31) {
DEBUG_SERIAL.println();
}
}
DEBUG_SERIAL.println();
#endif
digitalWrite(_cs, HIGH);
if (_spi) {
_spi->endTransaction();
}
return true;
}
bool write_then_read(uint8_t *write_buffer, size_t write_len,
uint8_t *read_buffer, size_t read_len,
uint8_t sendvalue = 0xFF);
Function prototype defines default value for 5th argument

## Slide 4
Read Cold Junction Temperature
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
CR0 Register
64
80

## Slide 5
setThermocoupleType
void Adafruit_MAX31856::setThermocoupleType(max31856_thermocoupletype_t type) {
uint8_t t = readRegister8(MAX31856_CR1_REG);
t &= 0xF0; // mask off bottom 4 bits
t |= (uint8_t)type & 0x0F;
writeRegister8(MAX31856_CR1_REG, t);
}
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
t
0xF0
t &= 0xFF
Bits 3 - 0 are forced to 0
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
CR1 Register | Reserved | AVGSEL2 | AVGSEL1 | AVGSEL0 | TCTYPE3 | TCTYPE2 | TCTYPE1 | TCTYPE0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
(uint8_t)type
0x0F
(uint8_t)type & 0x0F
Bits 7 – 4 are forced to 0
MAX31856_TCTYPE_K: 3
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
t
(uint8_t)type & 0x0F
t |= (uint8_t)type & 0x0F
Only bottom 4 bits are set to type

## Slide 6
setAveragingOff
void setAveragingOff() {
Serial.println("setAveragingOff");
uint8_t t = readRegister8(MAX31856_CR1_REG_READ);
Serial.println("t after readRegister8");
Serial.println(t);
//UPDATE LATER SO DIFFERENT AVERAGING SETTINGS BESIDES OFF CAN BE SET
uint8_t averagingType = 0x00;
t &= 0x0F; // mask off top 4 bits
t |= averagingType & 0xF0;
Serial.println("t after bitwise operations");
Serial.println(t);
writeRegister8(MAX31856_CR1_REG_WRITE, t);
}
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
t
0x0F
t &= 0x0F
Bits 7 - 4 are forced to 0
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
CR1 Register | Reserved | AVGSEL2 | AVGSEL1 | AVGSEL0 | TCTYPE3 | TCTYPE2 | TCTYPE1 | TCTYPE0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
(uint8_t)type
0xF0
(uint8_t)type & 0xF0
Bits 3 – 0 are forced to 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
t
(uint8_t)type & 0xF0
t |= (uint8_t)type & 0xF0
Only top 4 bits are set to type

## Slide 7
triggerOneShot
void triggerOneShot(void) {
//uint8_t t = readRegister8(MAX31856_CR0_REG); // get current register value
SPI.transfer(MAX31856_CR0_REG_READ);
uint8_t t = SPI.transfer(sendvalue);
Serial.print("MAX31856_CR0_REG_READ inside triggerOneShot: ");
Serial.println(t);
//Serial.print("triggerOneShot MAX31856_CR0_REG_READ: ");
//Serial.println(t);
t &= ~MAX31856_CR0_AUTOCONVERT; // turn off autoconvert
t |= MAX31856_CR0_1SHOT; // turn on one-shot
Serial.print("t after bit operations: ");
Serial.println(t);
//writeRegister8(MAX31856_CR0_REG, t); // write value back to register
SPI.transfer(MAX31856_CR0_REG_WRITE);
SPI.transfer(t);
delay(200);
}
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
t
MAX31856_CR0_AUTOCONVERT
t &= ~MAX61856_CR0_AUTOCONVERT
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
MAX31856_CR0_1SHOT
t |= MAX31856_CR0_1SHOT
Bits 3 – 0 are forced to 0
#define MAX31856_CR0_AUTOCONVERT 0x80 ///< Config 0 Auto convert flag
~MAX31856_CR0_AUTOCONVERT
#define MAX31856_CR0_1SHOT 0x40 ///< Config 0 one shot convert flag
Decimal 16
Bits 7 is forced to 0
t

## Slide 8
/**************************************************************************/
/*!
@brief Return hot-junction (thermocouple) temperature
@returns Floating point temperature in Celsius
*/
/**************************************************************************/
float Adafruit_MAX31856::readThermocoupleTemperature(void) {
// for one-shot, make it happen
if (conversionMode == MAX31856_ONESHOT) {
triggerOneShot();
uint32_t start = millis();
while (!conversionComplete()) {
if (millis() - start > 250)
return NAN;
delay(10);
}
}
Read Thermocouple Temperature
/**************************************************************************/
/*!
@brief Begin a one-shot (read temperature only upon request) measurement.
Value must be read later, not returned here!
*/
/**************************************************************************/
void Adafruit_MAX31856::triggerOneShot(void) {
if (conversionMode == MAX31856_CONTINUOUS)
return;
uint8_t t = readRegister8(MAX31856_CR0_REG); // get current register value
t &= ~MAX31856_CR0_AUTOCONVERT; // turn off autoconvert
t |= MAX31856_CR0_1SHOT; // turn on one-shot
writeRegister8(MAX31856_CR0_REG, t); // write value back to register
// conversion starts when CS goes high
}

## Slide 9
Read Thermocouple Temperature
//fix sign
if (temp24 & 0x800000) {
temp24 |= 0xFF000000;
}
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  |  |  |  |  | X | 1 | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
temp24
MAX31856_CR0_1SHOT
0x80 = 1000 0000
tcByteL
tcByteM
tcByteH
//fix sign
if(IsBit1(tcByte2,7)) {
//MSB is 1, this is a negative number.
//Because we only have 24 bits and are storing in a 32 bit container, add 8 1's to bits 31 - 24 so that when we later shift right by 5 bits the negative sign carries along
}
1
94
-32

## Slide 10
conversionComplete
return !(readRegister8(max31856SpiSettings,pin_CS,MAX31856_CR0_REG_READ) & MAX31856_CR0_1SHOT);
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
X | 1 | X | X | X | X | X | X
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
MAX31856_CR0_REG_READ
MAX31856_CR0_1SHOT
MAX31856_CR0_REG_READ & MAX31856_CR0_1SHOT
!(MAX31856_CR0_REG_READ & MAX31856_CR0_1SHOT) → false
Assume bit 6 = 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
X | 0 | X | X | X | X | X | X
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
MAX31856_CR0_REG_READ
MAX31856_CR0_1SHOT
MAX31856_CR0_REG_READ & MAX31856_CR0_1SHOT
!(MAX31856_CR0_REG_READ & MAX31856_CR0_1SHOT) → true
Assume bit 6 = 0
Ultimately, this operates on the following truth table
if bit 6 == 1
return false
else
return true
end